# SECTION 06 61 19 DIFINITI QUARTZ SURFACING FABRICATIONS

SECTION 12 36 61 DIFINITI QUARTZ COUNTERTOP

- - GENERAL

  - SUMMARY

    - Section Includes:

      - Quartz countertops.

      - Quartz [____].

      - Setting materials and accessories.

    - Related Sections:

      - Division 01: Administrative, procedural, and temporary work requirements.

      - Section [__ __ __ - _______] - Steel supports.

      - Section [__ __ __ - _______] - Wood supports.

      - Section [__ __ __ - _______] - Cementitious backer unit substrate.

      - Section [__ __ __ - _______] - Base cabinets.

      - Section [__ __ __ - _______] - Joint sealers.

      - Section [__ __ __ - _______] - Toilet Accessories.

  - REFERENCES

    - American National Standards Institute (ANSI):

      - A108.5 - Installation of Ceramic Tile with Dry-Set Portland Cement Mortar or Latex Portland Cement Mortar.

      - A118.4 - Latex-Portland Cement Mortar.

    - ASTM International (ASTM):

      - C97 - Standard Test Methods for Absorption and Bulk Specific Gravity of Dimension Stone.

      - C99 - Standard Test Method for Modulus of Rupture of Dimension Stone.

      - C170 - Standard Test Method for Compressive Strength of Dimension Stone.

      - C241 - Standard Test Method for Abrasion Resistance of Stone Subjected to Foot Traffic.

      - C482 - Standard Test Method for Bond Strength of Ceramic Tile to Portland Cement.

      - C484 - Standard Test Method for Thermal Shock Resistance of Glazed Ceramic Tile.

      - C531 - Standard Test Method for Linear Shrinkage and Coefficient of Thermal Expansion of Chemical-Resistant Mortars, Grouts, Monolithic Surfacings, and Polymer Concretes.

      - C648 - Standard Test Method for Breaking Strength of Ceramic Tile.

      - C650 - Standard Test Method for Resistance of Ceramic Tile to Chemical Substances.

      - C672/C672M - Standard Test Method for Scaling Resistance of Concrete Surfaces Exposed to Deicing Chemicals.

      - C880 - Standard Test Method for Flexural Strength of Dimension Stone.

      - C1026 - Standard Test Method for Measuring the Resistance of Ceramic Tile to Freeze-Thaw Cycling.

      - C1028 - Standard Test Method for Determining the Static Coefficient of Friction of Ceramic Tile and Other Like Surfaces by the Horizontal Dynamometer Pull-Meter Method.

      - E84 - Standard Test Method for Surface Burning Characteristics of Building Materials.

  - SUBMITTALS

    - Shop Drawings: Include layout, dimensions, materials, finishes, cutouts, and attachments.

    - Samples:

      - [4 x 4] [__ x __] inch quartz samples [in specified color.] [showing available colors.]

      - [3] [__] inch long joint sealer samples [in specified color.] [showing available colors.]

  - QUALITY ASSURANCE

    - Fabricator and Installer Qualifications: Minimum [2] [__] years [documented] experience in work of this Section.

    - Mockup:

      - Construct [countertop mockup, [6] [__] feet wide, full depth, with splash [and skirt].] [[____] mockup, [__] x [__] feet.]

      - Include [plumbing fixtures and trim.] [____.]

      - Locate [where directed.] [____.]

      - Approved mockup may remain as part of the Work.

- - PRODUCTS

  - MANUFACTURERS

    - Contract Documents are based on products by Terrazzo & Marble Supply Co.

    - Substitutions: [Under provisions of Division 01.] [Not permitted.]

  - MATERIALS

    - Quartz Sheet:

      - Product: DIFINITI.

      - Composition: Quartz aggregate, resin, and color pigments formed into flat slabs.

      - Color: [____.] [To be selected from manufacturer’s full color range.]

      - Thickness:

      - Physical characteristics:

        - Physical characteristics to meet all of the performance criteria of DIFINITI with regard to physical strength, chemical resistance, ease of maintenance and appearance.

  - ACCESSORIES

    - Adhesive: Type recommended by quartz manufacturer.

      - Epoxy or Polyester Adhesive tinted to match quartz surface: Akemi Professional Stone Products

  - FABRICATION

    - Cut quartz panels accurately to required shapes and dimensions.

    - All internal corners must be haveat least a 3/8” radius.

    - Seams should not exceed ¹⁄16” wide.

    - Cut holes for [sinks] [faucets] [toilet accessories] [____].

- - EXECUTION

  - PREPARATION

    - Clean surfaces to receive fabrications; remove loose and foreign matter than could interfere with adhesion.

  - INSTALLATION

    - Install fabrications in accordance with manufacturer’s instructions and approved Shop Drawings.

    - Adhere fabrications with continuous beads of adhesive.

    - Set plumb and level. Align adjacent pieces in same plane.

    - Install with hairline joints.

    - Fill joints between fabrications and adjacent construction with joint sealer; finish smooth and flush.

  - INSTALLATION TOLERANCES

    - Maximum variation from level and plumb: 1/8 inch in 10 feet, noncumulative.

    - Maximum variation in plane between adjacent pieces at joint: Plus or minus 1/16 inch.

  - CLEANING

    - Clean fabrications in accordance with manufacturer's instructions.

  - PROTECTION

    - Protect installed fabrications with nonstaining sheet coverings.

# END OF SECTION